## Slide 1: Industrial training in ecil,Hyderabad
Presented by
T.MADHUBABU
(M110448EE)

## Slide 2: Ecil Organization profile
1.Control system group
2.Computer maintenance group
3.Communication systems group
4.Components group
5.Strategic Electronics group
6.Instrument group

## Slide 3: Digital V/UHF RADIO
M7 VHF/UHF range of radios is designed for defense forces fulfilling a comprehensive range of demanding communication needs in the fixed, maritime, deployable applications.
High RF power: 50W AM, 100W FM
Multimode software defined radio
Electronic protection measures (EPM)
Continuous AM and FM coverage from 100MHz - 400MHz
Integrated Power Supply

## Slide 4
M7 is ideally suited for dual use operations
continuous AM and FM coverage from 100 to 400 MHz includes
118-137 MHz Commercial ATC
137-156 MHz Land Mobile band
156-163 MHz Maritime band and
225-400 MHz Military band.

## Slide 6: OPERATION
Radio can be operated in Two modes:
EPM (electronic protection measure) –DIGITAL
V/UHF XS
Non-EPM –DIGITAL V/UHF X
Radio can be operated in following ways:
Locally using the front panel controls and indicators
Remotely using an DIGITAL V/UHF series controller
Remotely using compatible control equipment

## Slide 7: Block diagram of v/uhf radio

## Slide 8: specifications
Harmonics
Modulation
Sensitivity
Selectivity
Frequency response
Distortion
squelch

## Slide 9: Remote control unit
The DIGITAL V/UHF C remote controller allows one or more DIGITAL V/UHF radios to be operated from a remote location
The Control Head can also be used separately as a Remote Controller
the desktop controller consists of an AC/DC power supply and an interface card.

## Slide 11: Tuning the Radio
Waveform Profiles
A waveform profile is a set of instructions stored in the radio that define a mode of operation and certain parameters associated with the mode. Up to 20 waveform profiles can be created and stored in the radio.
Frequency Preset
There are three methods of tuning the radio
Tuning Using the Current Waveform Profile
Tuning by Recalling a Stored Waveform Profile
Tuning by Recalling a Stored Frequency Preset

## Slide 12: Tuning Using the Current Waveform Profile

## Slide 13: Tuning by Recalling a Stored Waveform Profile

## Slide 15: Tuning by Recalling a Stored Frequency Preset

## Slide 17: E1 RADIO INTERCONNECT

## Slide 18: Features
E1-RIC provides a digital end-to-end connection between the radios and a digital VCCS using E1 data.
Digital Networks:
Consolidates digital audio, E&M and
RCMS for 29 channels onto a single E1 bearer
Fault tolerant distributed architecture for safety critical applications

## Slide 19: Analogue Networks:
Consolidates RCMS for 32 channels onto a single data port
Provides automatic main/standby 4-wire E&M switching

## Slide 20: General characteristics
Radio compatibility | E1 RIC compatible with PAE and M7 series radios
Channel supported | Each E1 RIC supports 8 simplex channels ,or 8 duplex channels
Undedicated Inputs and Outputs | 4 user configured inputs and outputs, monitored and controlled via RCMS (PAE MARC) are available.
Operating temperature Storage temperature | -20°C to +55°C -30°C to +70°C
E1 Characteristics | 2.048 M bits/s using a balanced 120 ohm electrical interface
Response times Voice latency E and M signaling RCMS data | 0.25 ms 4 ms 50 ms

## Slide 21: E1 time slots

## Slide 22: Functional Description
Voice and Signalling
Routing Conventions-Transmit Circuits
Routing Convocations - Receive Circuits
RCMS Data
Voice selection
Notes: squelch is a circuit function that acts to suppress the audio (or video) output of a receiver in the absence of a sufficiently strong desired input signal.

## Slide 23: MARC Functionality
RCMS data available in two formats:
It is available in time slot T31 of the E1 data stream that connects the VCCS. Any RCMS information required by the VCCS is decoded whilst passing the data on to the MARC application.
It is available in RS232 format on the facilities connector and the Auxiliary connector. (This is normally used in an analogue applications

## Slide 24: System configuration

## Slide 25: Configuration 1

## Slide 26: Configuration 2

## Slide 29: Thank you