## Slide 1
INDUSTRIAL TRAINING
BHEL –EDN BANGLORE
SARATH T.S
M110278EE

## Slide 2: STEAM TURBINE CONTROLS IMPLEMENTATION
BINARY CONTROLS
ATRS
TP
ATT
GAMP
ANALOG CONTROLS
EHTC
TSE
LPBP&GSPC

## Slide 3
CONTROL SYSTEM
Burner management
Hp by pass
Superheating
Air flow control
fuel control

## Slide 4: TURBINE PROTECTION
The turbine protection system can be actuated by any of the following trip system. 1.Hydraulic trip system.
2.Electrical trip system.
Both the trip system , when initiated, act on the hydraulic control system and cause trip oil pressure to collapse which in turn closes the emergency stop valves interceptor valves and control valves.

## Slide 5: 1.HYDRAULIC TRIP SYSTEM
The hydraulic trip system comprises of the following trip devices and actuation of any one of these devices trips the turbine.
Overspeed trip device-1.
Over speed trip device-2.
Vacuum trip device.
Hand trip lever-1(local).
Hand trip lever-2(local).

## Slide 6: 2. ELECTRICAL TRIP SYSTEM
The turbine trip automatically under any of the following conditions. The initiating signal in each case actuates both the channels.
1.Condensor pressure protection fsp & vsp.
2.Lube oil protection low.
3.Fire protection operated.
4.Hp exhaust pressure high.
5.Axial shift very high.

## Slide 7
6.Hpt/ipt top-bottom temp high.
7.Tg bearing metal temp very high.
8.Turbine trip switch operated.
9.Trip command initiated from atrs.
10.Trip command from gen mechanical protection.
11.Generator protection or master fuel trip relay energised.
12.Isolation of generator from grid.

## Slide 8: 1.SUB-GROUP SAFETY DEVICES
The automatic turbine tester for the safety devices consists of the following sub tests:
1.Remote trip device-1.
2.Remote trip device-2.
3.Overspeed trip device -1.
4.Overspeed trip device -2 .
5.Low vacuum trip device.
During normal trip the safety devices close the stop valves of hp & ip, via the tripping devices. The remote trip solenoid valves 1&2 actuate the tripping devices by stopping the supply of control fluid to them and opening the trip fluid circuit to drain simultaneously. All other tripping devices by opening the auxiliary trip fluid circuit to drain.

## Slide 9: 2.SUB-GROUP HP/IP VALVES
The stop and control valves are the final control elements of the safety devices and hence their serviveability is just as important as that of safety devices themselves.The testing of these valves in conjuction with the safety devices ensures that all elements, which must operate if an emergency trip is initiated, has been fully tested for seviceability. There are two combined hp stop valves and control valves and two combined ip stop valves and control valves.
1.Hpcv-1. 2.Hpcv-2. 3.Ipcv-1. 4.Ipcv-2.

## Slide 10: GAMP
Gamp covers following :
1.Generator gas drying.
2.Generator bearing exhaust.
3.Generator seal oil.
4.Main excitor.
5.Generator primary water cooling.
6.Mechanical generator protection.

## Slide 11: GENERATOR GAS DRYING
Besides water, hydrogen is also used in the generator as coolant. This is requires operation of some drives such as heater, drier fan and a co2 flash evaporator. These are realized in : sub loop control co2 flash evaporator, sub loop control gas drier and cold gas temperature control valve.

## Slide 12: GENERATOR PRIMARY WATER COOLING
THE HEAT GENERATED IN STATOR WINDINGS, TERMINAL BUSHINGS AND PHASE CONNECTORS IS DISSIPATED THROUGH DIRECT WATER COOLING.THIS REALISED IN THE SUB LOOP CONTROL OF PRIMARY WATER PUMPS.
THE PW TEMP CONTROL VALVE HAS THE TASK OF MAINTAINING THE INLET TEMP OF PRIMARY WATERTO THE STATOR WINDINGS AT PRESET VALUE.

## Slide 13: MECHANICAL GENERATOR PROTECTION
This functional unit initiates turbine tripping based on 2 out of 3 principle with functional checking feature on any of the following faulty/alarming conditions.

## Slide 14: SUGGESTIONS
Electr o-Magnetic relay system
Reliability
Hard wired
Space usage
PLC
Easy change in logic

## Slide 15
THANK U..!